Exercise 2

Inputs

Inputs used : i9 and i10
i9 is used to detect whether the glue gun is empty
i10 used to check if the glue gun is full

Asynchronous or Synchronous

i9 - When the glue gun is empty we need to refil it . The operation cannot be carried out further without recharging the glue gun.So inorder to recharge the glue gun, we need to interrupt the current execution of the program and call a subroutine.Hence it should be handled asynchronously.
Here we are using reacti because this situation has to be handled immediately when the glue runs off.
i10-The fillling up of the gluegunshould happen simultaneously hence It is handled synchronously.

Instructions

The VAL instruction used to handle are
-> reacti detector.empty,recharge – To handle if the glue gun runs out off glue
->closei – To start gluing
->openi – To stop gluing
->set board=board:shift(null by 10,10,0) – To sift the gluing to 10mm along the x and y directions
->wait sig(detector.end) – To check if the glue gun is full that is to check whether the i10 is high
->moves – It should move in a straight line

->To make sure that the object for which a glue default occurred is correctly glued along the whole trajectory is to check whether the tool has travelled through all the points A B C and D and has returned back to A